I G O R   E P S T E I N’S  K L E Z M E R - T O V

T R I O/QUARTETT

T E C H N I C A L   R I D E R

- One per side of a compact high quality speakers plus one per side sub bass unit driven from professional amplifiers with appropriate controllers.

Acceptable brands are:
Speakers - Meyer UPA1C/P, MSL2 CQ1, USW, D&B902/602,
Amplifiers - Crest, Lab Gruppen, Ameron/Crown, QSC etc.

The system must be extremely quiet and free from all ground hums and amplifier noise; the amplifiers must be isolated from the stage so that no fan noise is audible in the performance area.

- Two high quality low profile monitor wedges (max. 12" + 1" horn) by same manufacturer as above.

- Minimum 8 channel desk with phantom power switchable individually on channels (global phantom switching will not be acceptable due to nature of some inputs), with at least four auxiliary sends, and 4-band eq with at least two sweepable mids.

- At least four channels of 31-band graphic eq . One each for left, right arm monitor sends. If additional system elements such as center cluster or delays are in use additional 31-band eq for all elements.

- One stereo delay line for delaying the main system (approx. 10-20ms) to ensure acoustic image remains correctly aligned.

- One professional CD player patched to allow sends to the house as well as the monitor.

- One professional MD player patched to allow sends to the house as well as the monitor.

- One professional reverb unit (Lexicon PCM70/80/90, TCM2000/5000, no Alesis, SPX90 etc.)

- One professional multi effects unit (Lexicon PCM70, Yamaha SPX990/1000 no Alesis etc.)

- One professional Mic.(Shure SM58  Beta) with st.

- Two professional Mic. for Clarinette (B and Bass Cl.)

- Two DI -  Boxes for the E-Piano ( Stereo)

- One DI -  Box for the Guittare